## Slide 1: Concurrent execution with SpeedGoat
Multiple CPU usage

## Slide 2: The model
We have different (local) subsystems that generate inputs to a referenced system. The latter is a standalone model with the input, output and setup modules from SpeedGoat.
Rmk: The SpeedGoat modules NEED to be in an external model that is referenced because it doesn’t work otherwise (according to Martin from SG…)
Referenced system

## Slide 3: Setting up the model
Set the local subsystems to “treat as atomic unit”
Create a MATLAB sample time variable ts in the base workspace such that it can be read by both SG_MDL and SG_REF_IO models

## Slide 4: Setting up the model
In Simulink, open Configuration Parameters then set Fixed-step size with the sample time variable ts
Click Configure tasks (1) , enable explicit model partitioning (2) and add tasks (3)
1
2
3

## Slide 5: Setting up the model
Set the period as the sampling time for all tasks
Attribute each block to the tasks

## Slide 6: Monitor with Task Execution Time
Via “slrtExplorer” or by “tg.ModelStatus.TETInfo” in matlab command window